Introduction to Robotics and Mechatronics
GROUP 2.5
Benson Chalethu
Pietro Griffa
Ingvar Groza
PostLab 03
Q1
The peak-to-peak amplitude of the generated signal is 2,40V.
Q2
The DC offset is 1,76V.
Q3
The frequency is 2,1 kHz.
Q4
To measure a point (a while loop step) it takes a time of 4,167us (=0,004167ms), which translate to an execution speed of 240 kHz.
Q5
The minimum is 0,560V and the maximum is about 3V. The voltage range is [0,56 3] and the voltage resolution is 2,4V/4096 = 0,5859 mV.

---
Q6
Frequency [Hz]	Peak-to-peak voltage [V]
20	1,2
40	1,2
60	1,2
80	1,2
100	1,2
200	1,2
As we expected by how we built the resistive divider circuit, the ratio of output to input voltage remains constant to 1,2V , not varying with the input frequency.
The delay is calculated with the following equation:
Where we consider the number of samples (120) of which one period of the signal gets split off and the execution time needed for one iteration in the while loop (calculated in Q4).

---
Q7
Frequency [Hz]	Peak-to-peak [V]	Phase shift [°]	Phase shift [ms]
20	2,4	20	2,778
40	2,16	34	2,362
60	2	40	1,852
80	1,76	42	1,458
100	1,52	48	1,334
200	0,96	69	1,597
That’s a typical low-pass behavior. High frequencies get attenuated, low frequencies passed. Also high frequencies get a phase, they lag more the higher the frequency is.

---
Q8
It will lead to the opposite outcome resulting in Q7. Low frequencies will get attenuated and high frequencies passed. A high-pass filter.
Q9

---
Q10
Q12/Q13
Max phase shift is 90deg.
Gain at cut-off freq is 0.7071 or -3.0103dB.
Q14
No. It’s a linear time invariant system. Emphasis on linear, because the system only amplifies the input at its frequency. The frequency wont get modulated hereby.

---
Q11
The system clearly responds like a 1st order system. 1st order systems have a very distinct linear slope around t=0s.

---
Q15
We can see that the cut-off frequency of our analog filter lies around 85Hz. It’s where the phase is -45deg and magnitude around -3dB.