Introduction to Robotics and Mechatronics
GROUP 2.5
Benson Chalethu
Pietro Griffa
Ingvar Groza
PostLab 03
Q1
The peak-to-peak amplitude of the generated signal is 2,40V.
Q2
The DC offset is 1,76V.
Q3
The frequency is 2,1 kHz.
Q4
To measure a point (a while loop step) it takes a time of 4,167us (=0,004167ms), which translate to an execution speed of 240 kHz.
Q5
The minimum is 0,560V and the maximum is about 3V. The voltage range is [0,56 3] and the voltage resolution is 2,4V/4096 = 0,5859 mV.

---
Q6
Frequency [Hz]	Peak-to-peak voltage [V]
20	1,2
40	1,2
60	1,2
80	1,2
100	1,2
200	1,2
As we expected by how we built the resistive divider circuit, the ratio of output to input voltage remains constant to 1,2V , not varying with the input frequency.
The delay is calculated with the following equation:
Where we consider the number of samples (120) and the execution time of the while loop (calculated in Q4).

---
Q7
Frequency [Hz]	Peak-to-peak [V]	Phase shift [°]	Phase shift [ms]
20	2,4	20	2,778
40	2,16	34	2,362
60	2	40	1,852
80	1,76	42	1,458
100	1,52	48	1,334
200	0,96	69	1,597

---
Q8
Switching the position of the resistive and capacitive elements we would pass from a low-pass filter to an high-pass filter. This means we would observe a behavior opposite to what we observed in point Q7: the phase shift will decrease with increasing frequencies and the peak-to-peak values will increase.
Q9